## Slide 1: REACTANCE IN AN A.C. CIRCUIT
Combined effect of R,L and C

## Slide 2: REACTANCE IN SERIES
Application of Ohm’s law for D.C. Circuits
Application of Ohm’s law for A.C. Circuits
Peak Voltage R.M.S. Voltage
Peak Current
R.M.S. Current

## Slide 3
Resistive Circuits
I and V are in phase
Capacitive and Inductive Circuits
I and V are 90° out of phase

## Slide 4: COMBINATION OF REACTIVE AND RESISTIVE COMPONENTS
Find Voltage at each component using Ohm’s Law

## Slide 5
Length of arrow indicates the magnitude

## Slide 6
The angle of the Vector ET(θ) indicates the phase between the source voltage and current
From Pythagoras theorem,
ET=√ ER2 + EL2

## Slide 7: TIPS TO REMEMBER:
When Circuit is purely resistive, phase angle is 0 because V and I are in phase.
As XL increases, phase angle becomes greater
At 45°, R and XL are equal in value
When a circuit contains pure inductive reactance with no resistance, phase angle increases to 90°
I is same in a series circuit

## Slide 8
Voltage drop is directly proportional to R or X of that component
So, we can have X and R vectors proportional to voltage vectors
The combined effect of R and X is called as IMPEDANCE(Z)

## Slide 9: SERIES RC CIRCUIT
Draw Voltage Vectors and Resistance vectors

## Slide 11: REACTANCE IN PARALLEL CIRCUIT
Voltage in Parallel components is same

## Slide 13: REACTANCE IN PARALLEL CIRCUIT

## Slide 15: POWER
Power Dissipation in a Resistive Circuit has a non-zero value

## Slide 16: Power Dissipation in a Reactive Circuit
In a reactive circuit there is no average or net power loss

## Slide 17
Calculate power at each component by VI
Calculate Current
Calculate voltage at each component

## Slide 18
Power Factor= True Power/Apparent Power

## Slide 19: Conclusions regarding Power:
For pure resistive circuits
Power factor=1
For pure inductive circuit
Power factor=0
For heavy loads its important consideration that cables must be capable of handling the apparent power

## Slide 20: INTRODUCTION TO RESONANCE
Occurs in many fields and also in ELECTRONICS
Device produces broadening or damping effect at resonance
RADIO and TV RECEIVERS—TUNE at a particular frequency because of resonance.
Tuning Circuit-C parallel L

## Slide 21: OVERVIEW FROM PRACTICAL CLASS
Parallel tuned ckt—Zmax
Condition for Resonance
R doesn’t effect Fr
Resonant Circuits not used in audio bands of frequencies