## Slide 1: GENERATION OF POLYPHASE VOLTAGES

## Slide 2: REQUEST TO PLEASE NOTE DOWN MOST OF THE TOPICS

## Slide 3
What is Single phase and polyphase supply
3 Phase supply

## Slide 4
Single phase voltages- consist of single alternating current or voltage waveform
One armature winding
No. of armature winding increased to make it polphase
No. of independent voltage waveform= no. of winding or phases
Angle between winding
Poly- phase=== many windings

## Slide 5
360/N
N=no. of windings or armature
3 phase most commonly used
Others could also be used

## Slide 6
For transmitting large powers three phase are generally used
Reasons for its popularity:
(i) it is more efficient
(ii) it uses less material for a given capacity

## Slide 8
Ea = Em sinωt ... (i)
Eb = Em sin(ωt −120°) ... (ii)
Ec = Em sin(ωt − 240°)……(iii)
Ea+Eb+Ec=0

## Slide 9: Phase Sequence
phase order or phase sequence a→b→c

## Slide 10
Rotation of the Field structure reversed A-c-b
By repeating the letters, this phase sequence can be written as acbacba which is the same thing as cba. Obviously, a three-phase system has only two possible sequences : abc and cba (i.e. abc read in the reverse direction).

## Slide 11: INTERCONNECTION OF THREE PHASES
Each phase or circuit would need two
conductors, the total number of conductors, in that case,being six.
Each transmission cable would contain six conductors which will make the whole system complicated and expensive

## Slide 12
Interconnected
Resulting in substantial saving of copper.
The general methods of interconnection are
(a) Star or Wye (Y) connection and
(b) Mesh or Delta ( Δ ) connection.

## Slide 13: Star or Wye (Y) Connection

## Slide 14
The point N is known as star point or neutral point.
point
N are replaced by a single conductor known as neutral conductor
four-wire, 3-phase system
If this three-phase voltage system is applied across a balanced symmetrical load, the neutral wire will be carrying three currents which are exactly equal in magnitude but are 120° out of phase with each
other. Hence, their vector sum is zero.
i.e. IR + IY + IB = 0
The p.d. between any terminal (or line) and neutral (or star) point gives the phase or star voltage
But the p.d. between any two lines gives the line-to-line voltage or simply line voltage.

## Slide 16: Voltages and Currents in Y-Connection
The voltage induced in each winding is called the phase voltage and current in each winding is likewise known as phase current.
However,the voltage available between any pair of terminals (or outers) is called line voltage (VL) and the current flowing in each line is called line current (IL ).