## Slide 1
SEMICONDUCTOR FUNDAMENTALS

## Slide 2: Commonly used forms in electronics
Diodes
Transistors
Integrated Circuits
And many others

## Slide 3: Advantages of Semiconductors
Small size and weight
Low power consumption
High efficiency
Great reliability
Instant operation when power is applied
Economic mass production

## Slide 4: Disadvantages of Semiconductors
Great susceptibility to change in temperature
Extra components required for stabilization
Easily damaged by heat when soldering into a circuit

## Slide 5: Semiconduction in Germanium and Silicon
Semiconductor materials
  Possess characteristics that fall between those of insulators and conductors
Pure semiconductor elements
  Carbon (C)
  Germanium (Ge)
  Silicon (Si)
    Used for most semiconductor devices

## Slide 6: Germanium
A powder of Germanium dioxide is recovered from ashes of certain coals and then reduced to solid form of Germanium

## Slide 7: Silicon
Found extensively in earth’s crust in silicon diode.
Found abundantly in sand, quartz, agate in form of silicon dioxide (silica) and chemically reduced to pure silicon.

## Slide 8: Semiconduction in Germanium and Silicon (cont’d.)
Figure 19-1. Atomic structure of silicon.

## Slide 9
Figure 19-3. Crystalline structure of silicon with covalent bonding.

## Slide 10
The covalent bond cannot support electrical activity because of its stability
At room temperature , pure silicon crystals are poor conductors and behave like insulators
After heat applied and temperature increased

## Slide 11: Semiconduction in Germanium and Silicon (cont’d.)
Negative temperature coefficient
  As temperature increases, resistance decreases
Heat
  Potential source of trouble for semiconductors
  Electrons break their covalent bonds

## Slide 12
Effect of temperature on Ge
Ge in heat sensitive devices

## Slide 13
Figure 19-4. A hole is created when an electron breaks its covalent bond.

## Slide 14: Conduction in Pure Germanium and Silicon (cont’d.)
Figure 19-5. Current flow in pure semiconductor material.

## Slide 15: Conduction in Doped Germanium and Silicon
Doping
  Adding impurities to a semiconductor material
Pentavalent
  Made of atoms with five valence electrons
Trivalent
  Made of atoms with three valence electrons

## Slide 16: Conduction in Doped Germanium and Silicon (cont’d.)
N-type material
  Pentavalent materials
  Electrons are the majority carrier
  Holes are the minority carrier
  Donor atoms

## Slide 17
Figure 19-6. Silicon semiconductor material doped with an arsenic atom.

## Slide 18: Conduction in Doped Germanium and Silicon (cont’d.)
Figure 19-7. Current flow in N-type material.

## Slide 19: Conduction in Doped Germanium and Silicon (cont’d.)
P-type material
  Trivalent materials
  Holes are the majority carrier
  Electrons are the minority carrier
  Acceptor atoms

## Slide 20
Figure 19-8. Silicon semiconductor material doped with an indium atom.

## Slide 21: Conduction in Doped Germanium and Silicon (cont’d.)
Figure 19-9. Current flow in P-type material.