## Slide 1: Chapter 1
Fundamentals of Electricity

## Slide 2: Objectives
After completing this chapter, you will be able to:
  Define atom, matter, element, and molecule
  List the parts of an atom
  Define the valence shell of an atom
  Identify the unit for measuring current
  Draw the symbol used to represent current flow in a circuit

## Slide 3: Objectives
Describe the difference between conductors, insulators, and semiconductors
Define difference of potential, electromotive force, and voltage
Draw the symbol used to represent voltage
Identify the unit used to measure voltage
Define resistance

## Slide 4: Objectives
Identify characteristics of resistance in a circuit
Identify the unit for measuring resistance
Draw the symbol used to represent resistance in a circuit

## Slide 5: Matter, Elements, and Compounds
Matter
  Anything that occupies space
  Can be an element or compound
Element
  Basic building block of nature
Compound
  Chemical combination of two or more elements

## Slide 6
Figure 1-1. The chemical combination of two or more elements is called a compound. A molecule is the chemical combination of two or more atoms. Examples are water (H2O) and salt (NaCl).

## Slide 7: Matter, Elements, and Compounds (cont’d.)
Atom
– Smallest particle of an element
Molecule
  Chemical combination of two or more atoms
  Smallest part of a compound
Mixture
  Physical combination of elements and compounds

## Slide 8: A Closer Look at Atoms
Figure 1-2. Parts of an atom.

## Slide 9: A Closer Look at Atoms (cont’d.)
Atomic number
  Distinguishes one element from another
  Number of protons in the nucleus
Atomic weight
  Mass of the atom
  Sum of protons and neutrons

## Slide 10
Figure 1-3. The electrons are held in shells around the nucleus.
.

## Slide 11: A Closer Look at Atoms (cont’d.)
Valence shell
  Outer shell of an atom
Conductors
  Contain a large number of free electrons
Insulators
  Prevent the flow of electricity
  Absorb valence electrons from other atoms

## Slide 12: A Closer Look at Atoms (cont’d.)
Semiconductors
  Can function as conductors or insulators
Ionization
  Process of gaining or losing electrons

## Slide 13: Current
Current (I)
  Flow of electrons from negatively charged atoms to positively charged atoms
  Measured in amperes (A)
Coulomb (C)
  Charge of 6.24 x 1018 electrons

## Slide 14: Voltage
Potential
  Ability of source to perform electrical work
Difference of potential
  Referred to as electromotive force (emf) or voltage
Voltage (E)
  Force that moves electrons in a circuit
  Measured in volts (V)

## Slide 15: Voltage (cont’d.)
Figure 1-8. Electrons flow in a circuit because of the difference of potential.

## Slide 16: Resistance
Resistance (R)
  Opposition to current
  Measured in ohms (Ω)
Conductors
  Low resistance; possess many free electrons
Insulators
  High resistance; have few free electrons

## Slide 17: Summary
Matter can be an element or a compound
The atom consists of protons, neutrons,
and electrons
Key electronic concepts in this chapter:
– Ionization, current, voltage, resistance,
conductors, insulators

## Slide 18: Summary
The flow of electrons is called current
Current can encounter opposition, called
resistance