## Slide 1: OPTOELECTRONICS

## Slide 2
Device interact with electromagnetic spectrum
Three types of devices
Light Detection devices
Light conversion devices
Light emitting devices

## Slide 3
Semiconductor material and doping techniques determine relevant light wavelength for a device

## Slide 4: Basics Principles of Light
Light travels in form of radio waves
Light measured in wavelength
Speed= 1.86 * 10^5 miles per second
=3 * 10^8 m/sec
Frequency range of light=300 to 3 * 10^8 GHz
Visible range= 4*10^5 to 7.5*10^5 GHz
IR below 4*10^5 GHz
UV above 7.5*10^5 GHz
Light waves at upper end of frequency range have more energy than light waves at the lower end

## Slide 5: LIGHT SENSITIVE DEVICES
Photoconductive Cell (Photo Cell)
Made of light sensitive material- CdS or CdSe on an insulating substrate of Glass or ceramic
R varies from several 100 Ω to several 100 mΩ
Can withstand high operating voltages 200 to 300 Volts, with low power consumption of upto 300 mW.
Disadvantage:
--Slow response to light change

## Slide 7: λ represents light sensitive device
Symbol for Photocell

## Slide 8: Usage of Photocells
Light meters
Instrusion detectors
Automatic door openers
Equipments to test light intensity

## Slide 9: Photovoltaic Cell (Solar cell)
Converts Light energy into electrical energy
Solar Cells -> in converting solar to electrical
Majorly from silicon

## Slide 10: Construction of Solar Cell
Designed with large surface area
Metal support and metal contact act as electrical contacts

## Slide 11
Solar Cell is a highly inefficient device
Top efficiency of 15% to 20%
Solar Cells have low voltage output= 0.45 Volt at 50 mA
Must be connected in series and parallel n/w to obtain Desired V and I output.

## Slide 12: Applications of Solar cells
Light meters for photographic equipment
Motion picture projector soundtrack decoders
Battery chargers on satellite

## Slide 13
Schematic Symbol for a solar cell

## Slide 14: PHOTODIODE
Construction similar to a solar Cell and primarily from Silicon
Used same way as a solar cell, (Light variable resistor)

## Slide 15: Constructed in two ways

## Slide 16: Operation of PN Junction Diode
Same principle as a photovoltaic cell, except that it is used to control current flow and not generate it
R.B. across photodiode forming wide depletion region

## Slide 17: PIN Photodiode
Intrinsic layer effectively extends the depletion region
Responds to lower light frequencies(less energy)
PIN photodiode more efficient over a wider range

## Slide 18: Advantages of photodiode
Fast response to light changes, fastest of any photosensitive device
Disadvantages of photodiode
Low output compared to other photosensitive devices

## Slide 19: Photodiode Package

## Slide 20
Schematic symbol of Photodiode
Voltage Divider using a photodiode

## Slide 21: Phototransistor
Constructed like other transistors with 2 P-N junctions
Resembles standard NPN transistor
Packaged and used like a photodiode but has 3 leads
Equivalent circuit of Phototransistor

## Slide 22: Phototransistor Schematic Symbol

## Slide 23: Applications of Phototransistors
Photo tachometer
Photographic exposures controls
Flame detectors
Object counters
Mechanical positioners

## Slide 24: Light Emitting Devices
Convert electrical energy to light energy
Unlimited life span
Frequency of emitted light determined by
Type of semiconductor material
Regular diode do not emit light
Light visible because LED packaged in semitransparent material

## Slide 25
GaAs- infrared region
GaAsP-visible red light
By changing phosphide content different frequencies produced
LEDs avalaible in colors- Infrared, red, orange, yellow, green, blue, ultraviolet, pink, purple and white.

## Slide 26: LED Construction

## Slide 27: Common LED Packages

## Slide 28
F.B. must exceed 1.2 V
Series resistor

## Slide 30
SEVEN SEGMENT DISPLAY
For digital readouts

## Slide 31: Optical Coupler allows one circuit to pass a signal to another circuit while providing a high degree of electrical insulation